## Slide 1
Probabilistic Inverse Dynamics for Nonlinear Blood Pattern Reconstruction
Benjamin Cecchetto, Wolfgang Heidrich
University of British Columbia
Notes: 1

## Slide 2: Problem Scenario

## Slide 3
Problem Assumptions
Particles travel under ballistic motion with or without drag
Have noisy measurements of each particle after some distance that help with the reconstruction
Want to reconstruct the region of origin at the moment the particles separate
Notes: 3

## Slide 4: Specific Case: Blood Pattern Reconstruction
Blood drops obey ballistic motion
  Directions can be estimated from blood stains
  Used in forensics to reconstruct the region where someone was shot/stabbed

## Slide 5
Overview
Region of origin reconstruction given impact parameters
  Trajectory review
  2D PDF formulation
  3D PDF formulation
Bloodstain Parameter estimation
  Obtain impact angles
  Obtain speeds
  Obtain mass and drag coefficients
Notes: 5

## Slide 6
Overview
Region of origin reconstruction given impact parameters
  Trajectory review
  2D PDF formulation
  3D PDF formulation
Bloodstain Parameter estimation
  Obtain impact angles
  Obtain speeds
  Obtain mass and drag coefficients
Notes: 6

## Slide 7
Previous Work
Linear Region of Origin Estimation/Tangent Method
  Backtrack Software http://www.physics.carleton.ca/carter/
  AL Carter et. al ,Validation of the Back-Track Suite of Programs for Bloodstain Pattern Analysis. 2006.
  MB Illes et. Al, Use of the Backtrack Computer Program for Bloodstain Pattern Analysis of Stains From Downward-Moving Drops. 2005.
Linear Estimate
Actual
Notes: 7

## Slide 8
Previous Work - Limitations
Assumes particles travel in straight lines
No error estimate
Linear Estimate
Actual
Notes: 8

## Slide 9
Trajectory Review
Motion with Drag
Notes: 9

## Slide 10
Trajectory Reconstruction
Needed parameters
Having all parameters fix the trajectory
Notes: 10

## Slide 11
2D PDF formulation
Doesn't take into account noisy error in measured velocity
Introduce a new final velocity by adding the measurement error
  Use to generate new trajectories
  Each trajectory has a probability associated with it
    Assume normally distributed noise in measurements
Angle Error
Speed Error
=(0,0)
Notes: 11

## Slide 12
2D PDF formulation
Look at neighbouring trajectories with different final speed, angle
Approximate with non-warped Gaussian
Vary angle
Vary
speed
Notes: 12

## Slide 13
2D PDF formulation
Probability region gets more uncertain the further backwards in time the estimate
  Scale:
Notes: 13

## Slide 14
2D PDF formulation
Integrate over all times to obtain a PDF of where a single particle is likely to have been
Notes: 14

## Slide 15
Using PDFs to Estimate Area of Origin
Multiply PDFs for different particles to obtian PDF of where all particles likely to have been
Notes: 15

## Slide 16
Without Given Impact Speed
Prior that speeds at region of origin are similar
  Vary the speed over some interval, integrate the PDFs
Notes: 16

## Slide 17
Without Given Impact Speed
Notes: 17

## Slide 18
Obtaining 3D Area of Origin
Trajectory equations are separable in xz and yz planes
Construct a 3D PDF by element multiplying 2D PDFs
Notes: 18

## Slide 19
Overview
Region of origin reconstruction given impact parameters
  Trajectory review
  2D PDF formulation
  3D PDF formulation
Bloodstain Parameter estimation
  Obtain impact angles
  Obtain speeds
  Obtain mass and drag coefficients
Notes: 19

## Slide 20
Bloodstain Parameter Estimation
Notes: 20

## Slide 21
Bloodstain Direction Estimation
Fitting an ellipse gets us position and angle
  K. Boonkhong et. Al, Impact angle analysis of bloodstains using a simple image processing technique. 2010.
  Manually fit ellipses in BackTrack
Notes: 21

## Slide 22
Bloodstain Direction Estimation
Stain properties
  Need to fit ellipse to main stain
Main
Stain
Satellite
Stains
Notes: 22

## Slide 23
Bloodstain Direction Estimation
Get rid of satellite stains
  Exploit visibility property of convex regions
X
Notes: 23

## Slide 24
Bloodstain Direction Estimation
Perform visibility tests on mask
  Assume main stain is where the largest inscribed circle is
Notes: 24

## Slide 25
Bloodstain Mass and Drag Coefficient Estimation
Want to know the mass and drag coefficient
Know ellipse fit, half of minor axis is radius
  Can estimate sphere volume
Notes: 25
Mu = dynamic viscocity for air

## Slide 26
Bloodstain Speed Estimation
Projected blood drop image density is a function of
  Impact angle
  Speed of impact
Can invert and solve for speed
Notes: 26

## Slide 27
Experimental Results – Speed Estimation
Fit to Model
Physical Experiment Data
Notes: 27

## Slide 28
Experimental Results – Ellipse Fits
Notes: 28

## Slide 29
Synthetic Experiments – Error in Reconstruction

## Slide 30
Synthetic Experiments – Error in Reconstruction

## Slide 31
Experimental Results – Parabolic Reconstruction
Notes: 31

## Slide 32
Experimental Results – Parabolic Reconstruction
Notes: 32

## Slide 33
Experimental Results – Parabolic Reconstruction
Notes: 33

## Slide 34
Limitations/Future Work
Volume Loss
Similar speed prior
Only handles one area of origin
Only support error in velocity estimate
Notes: 34

## Slide 35
Conclusion
Accurate, modular new method to estimate area of origin from directions, positions which may or may not be used with more parameter estimates
New robust stain processing method to help with obtaining ellipses
New model to estimate speeds from stains
Notes: 35

## Slide 36
Thank you!
Questions?

## Slide 37
Directional Ambiguity
Notes: 37

## Slide 38
Error Bound
Notes: 38

## Slide 39
Experimental Results - Calibration
Notes: 39