## Slide 1: Glare encoding of high dynamic range images
Glare encoding
Mushfiqur ‘Nasa’ Rouf Rafał Mantiuk Wolfgang Heidrich Matthew Trentacoste Cheryl Lau
Single-shot HDR
Glare encoding
Reconstruction
IEEE Computer Vision and Pattern Recognition 2011
Notes: We propose a novel method to capture HDR imagery with a single image using structured glare
Exposure saturates
Shorter exposure...
We encode saturation info in the structured glare
Decode with our algorithm

## Slide 2: High Dynamic Range Imaging
[http://en.wikipedia.org/wiki/High_dynamic_range_imaging]
Notes: Natural scene
SKIP Displaying issues
Broad range of values
Dynamic range = ratio

## Slide 3: Motivation
Regular exposure
Shorter exposure
Shorter exposure
Shorter exposure
Glare encoding
Single-shot HDR
Reconstruction
Traditional: multiexposure | Our method: single exposure
single device
off-the-shelf
Shorter exposure
Scene
Clipped highlight
Notes: Exposure saturates
Shorter exposure...
We encode saturation info in the structured glare
Decode with our algorithm

## Slide 4: Previous work
Other methods
Multiple Exposures
  [Debevec and Malik 1997]
  [Mitsunaga and Nayar 2000]
  [Gallo et. al]
Spatial tradeoff
  Assorted pixels [Nayar and Mitsunaga 2000] [Nayar and Narasimhan 2005]
Temporal tradeoff
  (A)synchronous self-reset [El Gamal 2002] [Kitchen and Bermak 2004]
Our method
Single exposure
Full spatial resolution
Single exposure
[Nayar and Narasimhan 2005]
[Debevec and Malik 1997]
Notes: Most common
Ghosting

## Slide 5: Motivation
Good quality sensor dynamic range ≈ 12 f-stops
Natural scenes mostly <12 f-stops
  Except 2–5% of the brightest pixels
For only 2–5% pixels: expensive HDR sensor is impractical
Our solution: information encoding!
Chart: % of pixels with different dynamic range
| 3 | 6 | 9 | 12 | 15 | over 15
% of pixels | 7.5 | 30.5 | 42 | 18 | 1.5 | 0.5
F-stops

## Slide 6: Computational photography for HDRI
Optical encoding
  Glare = encode(intrinsic highlights)
  Captured image = intrinsic LDR + glare
  (highlights get clipped)
Computational decoding
  Estimate glare using priors
  Intrinsic LDR = captured image – glare
  Intrinsic highlights = decode(glare)

## Slide 7: Cross-screen filter to the rescue
Common photographic filter
Point spread function
Scene
Captured
No camera modification
Off-the-shelf filter

## Slide 8: Cross-screen filter to the rescue
Point spread function
No camera modification
Off-the-shelf filter
Blur strong yet invertible
  “Easy” to deconvolve
Tomography, instead of deconvolution

## Slide 9: Principle of tomographic reconstruction
Assuming we have estimated the glare...
Iterative reconstruction: SART
Glare
Clipped highlight

## Slide 10: Image formation model

## Slide 11: Formation of star-shaped glare
Filter
Lens
Sensor
Grooves on filter spread light
Notes: How the filter works... Focused rays...
Groove spreads... Parallel grooves...
Multiple directions...
... a convolution ...

## Slide 12: Formation of star-shaped glare
Lens
Grooves on filter spread light
Glare created on a line around a point
Multiple directions of grooves on filter make the star shape
Filter
Sensor
Notes: How the filter works... Focused rays...
Groove spreads... Parallel grooves...
Multiple directions...
... a convolution ...

## Slide 13: Computational decoding
Glare estimation
Glare removal
Tomography

## Slide 14: Filter point spread function
Collection of 1D filters  only 1D processing
  Possible to process one row at a time
Sensor
Log magnitude
Notes: That’s the image ...
Glare pattern... Also kernel
LOG PLOT
Collection of 1D filters

## Slide 15: Filter point spread function – 1D
Dirac peak preserves spatial frequencies => invertible
Glare falloff encodes brightness
Linear in log space
X
Log magnitude
  Dirac peak
  4 orders of magnitude
Sensor
Notes: LOG PLOT
Linear in log scale = exponential

## Slide 16: Filter point spread function – 1D
=
+
X
log
β
X
log
α
X
log
α+β
+
linear
X
Linear in log space
  Dirac peak
Residual
NOT shift-invariant
(Filter)
Notes: Split our kernel...
LOG PLOT
Convolution tends to destroy information but...

## Slide 17: Glare estimation – formulation
+residual + noise
Express captured image in terms of intrinsic image
Find intrinsic image by minimizing an energy function
Captured g
=
Intrinsic f
Glare K *f
+
Clipped
Gradients show a heavy-tailed distribution
[Levin et. al 2007]
Glare
+
Constraints on r
Next: transform this deconvolution into tomography
Notes: Back to the split kernel
Simulated scenario...
AUTO....
R is not a convolution per se...
Ignore noise
Need prior information...
Sparse prior

## Slide 18: Glare estimation – line integrals
Aggregate glare
Log magnitude
Glare line: linear in log space
X
Superimposed glare
gives aggregate brightness: line integral  tomography
has the same linear-in-log-space structure:
Image prior!
Glare
Clipped highlight
Glare row
Notes: The exponential falloff observation acts as a powerful prior...
Linear in log space

## Slide 19: Glare estimation – estimating line integrals
Image prior!
Log magnitude
Relating line integrals with glare
X
Saturated pixels
M
Unsaturated pixels
Saturated pixels
u
completely describe total glare
Run: For each M, on each row, for each glare direction
Notes: Instead of solving this equation directly, we use the exponential falloff prior here
For some set of unsaturated pixels in a row ...
(uncover the final equation term by term)

## Slide 20: Computational decoding
Glare estimation
Glare removal
Tomography

## Slide 21: Glare removal
Glare estimation yields:
LDR only!
Next: reconstruct clipped highlights
Captured g
–
Glare βK * f + γr
=
Intrinsic (LDR) f

## Slide 22: Computational decoding
Glare estimation
Glare removal
Tomography

## Slide 23: Tomography
Line integral estimates
give aggregate information about clipped pixels
SART tomography
gives the HDR reconstruction
Clipped pixels
Glare
HDR part
LDR part
1D projection of
2D unknown region

## Slide 24: Results and discussion

## Slide 25: Results – starbucks
Input
LDR part
HDR part | DR increase: 9.21 f-stops
Reference
Reconstruction
Clipped

## Slide 26: Results – science world
Reference
Input
Reconstruction
LDR part
HDR part | DR increase: 5.41 f-stops

## Slide 27: Results – car
Input
Reconstruction
LDR part
HDR part | DR increase: 6.31 f-stops

## Slide 28: Discussion
Deconvolution vs. SART Tomography
  Good encoding => large energy spread => large PSF
  Large linear system
  Control over reconstruction
  Noise amplification
  SART as a regularizer
Limited # of views => Small saturations
Highlights need to be sufficiently bright

## Slide 29: Conclusion
Optically encode structured patterns of glare with a cross-screen filter
  Preserves frequencies
  Is 1D separable
Computationally decode
  Image prior: log-linear glare falloff
  Sparse gradient prior: L1 optimization in gradient domain
  Tomography, not deconvolution!
First single-shot HDRI with off-the-shelf technology

## Slide 30
Thank you
Sponsored by

## Slide 31: Future work
Video
Other priors
  cross channel correlation

## Slide 32: Results – street
Input
Reconstruction
LDR part
HDR part

## Slide 33: Results – desk
Reference
Input
Reconstruction
LDR part
HDR part

## Slide 34: Results – building
Input
Reconstruction
LDR part
HDR part
Reference

## Slide 35: Constraints on residual glare R
Input
Without R
With R
Reconstruction

## Slide 36: Extra slide on limits of brightness
Chart from suppl.

## Slide 37: Something on Noise
Chart from suppl.

## Slide 38: Addition in linear domain?

## Slide 39: Application
HDRI
Environment maps
?
?
Add images
Notes: (Motivate the audience here...)

## Slide 40: Image formation model
=
+
X
log
β
X
log
α
X
log
α+β
+
linear
X
Linear in log space
  Dirac peak
Residual
NOT shift-invariant
Notes: Split our kernel...
LOG PLOT
Convolution tends to destroy information but...

## Slide 41: HDR Imaging : HOWTO
Multiple Exposures
Space Tradeoff
  [nayar and Narasimhan 2005]
[http://www.hdrsoft.com]
Replace
Need to add references here?
Notes: Most common
Ghosting

## Slide 42: HDR Imaging : HOWTO
Multiple Exposures
Space Tradeoff
  Assorted Pixels
  [nayar and Narasimhan 2005]
Need to add references here?
Notes: Camera sensor array
Besides R G B samples...
Demosaicing...
alternately size of pixel...

## Slide 43: Overview
Tomography
Captured
LDR part
L1 Optimize
Recovered
HDR part
Glare
replace
Virtual low exposure
Cross-screen filter
Virtual low exposure
Scene
LDR capture Virtual low exposure
Notes: We use the star filter..
Our algorithm is an optimization..
Separates the glare and does tomography
(need to add a glare image here)

## Slide 44: Motivation
98% Scene DR < Sensor DR = 103.5 (~12 f-stops)
Can it be done with one snapshot?
Chart: % of pixels with different dynamic ranges
| 10^1:1 | 10^2:1 | 10^3:1 | 10^4:1 | 10^5:1 | 10^6:1
% of pixels | 7.5 | 30.5 | 42 | 18 | 1.5 | 0.5
Dynamic range

## Slide 45: Glare estimation – complete formulation
+residual + noise
We need priors to decode information
Captured g
=
Original f
Glare
+
Clipped
Natural Images have edges and smooth regions
Gradients show a heavy-tailed distribution
[Levin et. al 2007]
L1 optimization in gradient domain
Glare too dim
Notes: Back to the split kernel
Simulated scenario...
AUTO....
R is not a convolution per se...
Ignore noise
Need prior information...
Sparse prior

## Slide 46: Motivation
Filter Profile
Encode information!
98% Scene DR < Sensor DR = 103.5 (~12 f-stops)
HVS cannot capture details in highlights
  Accurate reconstruction not necessary
Can it be done with one snapshot?
CVPR 2011 | Glare Encoding of High Dynamic Range Images
Notes: Human Visual System ....
... Such as Environment map
We want to Encode
Cheryl’s one page abstract