## Slide 1: All-Hex Mesh Generation via Volumetric PolyCube Deformation
James Gregson1, Alla Sheffer1 and Eugene Zhang2
1University of British Columbia,
2Oregon State University
(Fully Automatic)

## Slide 2: Motivation
Quality all-hex meshes:
  perform better in some areas
  are commonly used
  can take weeks to build
Industry needs automatic all-hex meshing
Courtesy: General Fusion
1

## Slide 3: Mesh Quality
Ideal hex is perfect cube
  Low mapping distortion
Ideal mesh is regular
  Efficient
2

## Slide 4: Mesh Quality
Ideal hex is perfect cube
  Low mapping distortion
Ideal mesh is regular
  Efficient
One bad hex can make a mesh unusable
3

## Slide 5: Previous Work: Hex-Meshing
Hex-dominant Meshing
  e.g. LpCVT, Levy & Liu 2010
  High mesh quality
  Many non-hexes (20%+)
    Requires specialized solvers
Lp CVT, Levy & Liu 2010
4

## Slide 6: Previous Work: Hex-Meshing
Grid & Octree Meshing
  e.g. Marechal 2009
  All-hex meshes
  Low minimum quality
    Requires specialized solvers
5

## Slide 7: Previous Work: Automatic PolyCubes
Existing automatic PolyCube methods
  Lin et. al. 2008, He et. al. 2009
  Don’t use distortion to find structure
  Don’t parameterize volume
Lin 2008
He 2009
Current
Current
6

## Slide 8: Method: Overview
Automatically builds PolyCubes
  Incorporating volumetric distortion
  Obtains volumetric parameterization
Uses PolyCubes as domains to:
  Build regular all-hex meshes
  Achieve high minimum hex quality
7

## Slide 9: Method: Rotation-Driven Deformation
Deforms models to PolyCube-like shapes
  Define PolyCube domain structure
  Makes hex-structure more obvious
8

## Slide 10: Method: Rotation-Driven Deformation
Iteratively aligns surface normals with XYZ axes
At each iteration:
  Computes volumetric deformation gradient field
  Integrates gradient field to deform model
Input
1 iteration
5 iterations
9

## Slide 11: Method: Rotation-Driven Deformation
Deformation gradients give 3 vector fields
  Orthogonal & surface-aligned
  Smooth & singularity free (proof in paper)
  Local UVW parameterization axis directions
U axis gradient
V axis gradient
Input cross-section
Deformation gradients
Input
Integrated
10

## Slide 12: Method: Rotation-Driven Deformation
Build mesh in UVW and map to XYZ
  Domain structure found automatically!
  Distortion accounted for!
UVW
XYZ

## Slide 13: Method: Position-Driven Deformation
Deformed models closely resemble PolyCubes
PolyCubes formed by:
  Segmenting surface by axis-alignment
  Enforcing planarity constraints on segmentation
deformed model
segmented model
after planarity constraints
11

## Slide 14: Our Method: Mesh Generation
Uniformly hex-mesh PolyCube
Map back using volumetric mapping
Add padding layer and optimize quality
after planarity constraints
uniformly meshed
mapped & optimized mesh
12

## Slide 15: Method: Position-Driven Deformation
PolyCube edges should be:
  Straight
  Axis-aligned
Criteria not always met
  Detected by edge extrema
  Modify segmentation in these areas
13

## Slide 16: Method: Position-Driven Deformation
Splitting charts inserted at edge extrema
  `Rotates’ corresponding portions of surfaces
Locally adds distortion to correct structure
14

## Slide 17: Results
Automatic meshing of complex objects with:
  All-hex elements
  High minimum quality
  Regular connectivity
15

## Slide 18: Results
Automatic meshing of complex objects with:
  All-hex elements
  High minimum quality
  Regular connectivity
16

## Slide 19: Mesh Quality: Min. Scaled Jacobian
Model | Marechal 2009 | PolyCube Deformation
 | 0.005 | 0.196
 | 0.016 | 0.131
 | 0.018 | 0.215
 | 0.056 | 0.105
 | 0.017 | 0.178
17

## Slide 20: Results
Improves upon previous work
  Minimum quality
  Mesh regularity
PolyCube Deformation
Marechal 2009
18

## Slide 21: Results
LS-DYNA ‘armor piercing’ stress test:
  Aluminum bunny, 2km/s steel projectile
19

## Slide 22: Limitations
No theoretical guarantees on
  Hex quality
  PolyCube validity
May smooth sharp features
Results depend on orientation
20

## Slide 23: Conclusions
Presented automatic all-hex meshing algorithm
  highly regular meshes
  high quality meshes (min. & avg.)
Key is PolyCube construction
  Automatically generates volumetric mappings
  Uses volumetric distortion to find domain structure
21

## Slide 24: Questions?